## Slide 1: PlaatEnergy (Energy Data Logger) Private Open Source Project
W.B.J. van der Plaat
(Software Architect)

## Slide 2: Question
How many energy is my house using daily?
How many gas is my heater using daily?
How many energy is my solar system deliver daily?
How many solar power is directly consume by my house?

## Slide 3: Idea
Lets create an application which measures everything
Records every minute energy and gas usage
Records every minute solar energy delivered
Records every minute environment temperature, humidity and pressure
Create User friendly Web GUI
Use low cost, low energy hardware

## Slide 4: Used hardware
Raspberry Pi 3B
USB to P1 Cable
Micro SD card (16GB)
USB power supply
Raspberry Pi Case

## Slide 5: Optional hardware
Wifi USB Dongle
Bluetooth USB Dongle
Pi Sense Hat
Unicorn Hat

## Slide 6
Raspberry Pi
PlaatEnergy
Pi Sense Hat
Wifi Router
Hardware view – Configuration 1
Ethernet
Omnik Solar
Converter
HDMI
USB
USB
Wifi

## Slide 7
Raspberry Pi
PlaatEnergy
Sense Hat
Omnik Solar
Converter
Digital Energy
Meter
Digital Gas
Meter
Wifi Router
Hardware view – Configuration 2
P1 cable
Ethernet
Wifi
Bluetooth
ADSL Router
Internet
PlaatEnergy
Reachable on
internet
Ethernet
UTP
USB

## Slide 8
Raspberry Pi
PlaatEnergy
Unicorn hat
Hosola Solar
Converter
Digital Energy
Meter
Digital Gas
Meter
Hosola Solar
Converter
Hosola Solar
Converter
Wifi Router
Hardware view – Configuration 3
Ethernet
Wifi
Wifi
Wifi
HDMI
Bluetooth
PlaatEnergy
Reachable on
internet
PlaatEnergy
slide show
at
monitor
P1 cable
ADSL Router
Internet
ethernet
UTP
USB

## Slide 9: PlaatEnergy Software Architecture
Solar Converter
Interface
Energy Meter
Interface
Environment
Interface
Display
Interface
Database Layer
Business Logic Layer
Presentation Layer
Google Charts
Weather Service
JSON
PHP/CSS/JS
PHP
MySQL
PHP/ “Python”
Operating
System
Debian Linux
Vendor Support
Omnik
Hosola
Vendor support
Kaifa
Landis
kamstrup
Vendor support
Pi Sense Hat
Unicorn Hat
Vendor support
Pi onboard
Pi Sense Hat
Apache

## Slide 10: PlaatEnergy Key features
Measure each device every minute
User friendly web interface
Show real-time, historical and forecast data
Show financial data
Support measurement corrections
Export measure data to CSV and SQL
Custom Data Report
Open Source and free to use!
Automatic data model patching when upgrading
Secure access to Web GUI and settings

## Slide 12: Conclusion
My energy use is dropped with 25%
My gas use is dropped with 50%
because I am more aware now.
PlaatEnergy is downloaded ca. 120 times “Customers” sending great feedback back 
SOS Solutions. One of the biggest Raspberry Pi resellers in the Netherlands will sell soon a Pi Smart Energy Kit with includes PlaatEnergy 

## Slide 21: PlaatProtect (Burglar / Fire Alarm Centre) Private Open Source Project
W.B.J. van der Plaat
(Software Architect)

## Slide 22: Next project - PlaatProtect
Burglar / Fire Alarm Centre running on Raspberry Pi
  Integrate Webcams
    Motion detection with auto recording
  Integrate Zigbee meshwork
    Control lights in my house (Philips Hue)
    Fire detector (Google Nest Protect)
  Push alarm notifications to Mobile
  Integrate Z-Wave meshwork
    IR detector(s)
    Alarm Horn
    Keypad

## Slide 23: PlaatProtect Software Architecture
Light
Interface
Zigbee
Interface
Z Wave
Interface
Webcam
Interface
Database Layer
Business Logic Layer
Presentation Layer
Google Charts
Notification Service
JSON
PHP/CSS/JS
PHP
MySQL
PHP/ “Python”
Operating
System
Debian Linux
Vendor Support
HUE Philips
Vendor support
Google Protect
Vendor support
Sony PS2 webcam
Vendor support
- Aeotec
- Aeon
Apache

## Slide 24: Used hardware
Philips Hue Bridge
Philips Hue Lamps / Strips
Z-Wave USB Dongle
Z-Wave Horn
Z-Wave IR detector
Z- Wave Keypad
Google Nest Protect
USB Webcam

## Slide 25
Raspberry Pi
PlaatEnergy
PlaatProtect
Sense Hat (Pi)
Solar
Converter
Digital Energy
Meter
Digital Gas
Meter
Wifi Router
Hardware view – Configuration 4
P1 cable
Webcam
1
Wifi
Bluetooth
ADSL Router
Internet
USB
USB
Z Wave
(mesh network)
Ethernet
Webcam
2
IR Detector(s)
Alarm
Horn
Wifi
Alarm
Push
Message
Keypad
with ID tags
USB
Ethernet
UTP
Zigbee
(mesh network)
Bulb
Light
Strip
USB